## Slide 1: SECS with Tcl
Jan Nijtmans
EuroTcl 2008, june 7

## Slide 2: Outline
How it started: automatic testing
SECS message protocol host <-> equipment
State storage in array
SECS commands
Demo

## Slide 3: SECS protocol
Semiconductor Equipment Communications Standard
Messages over RS-232 or TCP/IP
10-byte header followed by message
Request/Reply

## Slide 4: SECS message format
len dev cmd sub id
message ………………..
cmd odd: request
cmd even: reply
high bit: reply expected

## Slide 5: SECS messages
Types:
B: binary
A: ASCII
U1, U2, U4, U8, I1, I2, I4, I8
F4, F8
L
fmt len ………………

## Slide 6: Examples
B 0 1 2 3
A {this is a string}
L {B 0 1 2 3} {A {this is a string}}
U2 100 2000 3000
A this is a string
U1 1000 2000 -1  I2 1000 2000 -1

## Slide 7: ::secs::S6F5
proc S6F5 {sock dev cmd sub msg id} {
::secs::write $sock $dev [expr {$cmd+1}] $sub [list B 0] $id
}

## Slide 8: ::secs::write
::secs::write $sock $dev $cmd $msg $sub cb1
proc cb1 {sock dev cmd msg sub id} {
set cmd1 …..;set msg1 …..
::secs::write $sock $dev $cmd1 $msg1 $sub $cb2
}
proc cb2 {sock dev cmd msg sub id} {
set cmd2 …..;set msg2 …..
::secs::write $sock $dev $cmd2 $msg2 $sub $cb3
}

## Slide 9: ::secs::init
::secs::init host port arrayname
Set up connection

## Slide 10: ::secs::set
::secs::set EQP {L {U1 5} {U2 1000}} \
[L {F 3.5} {B 45 46 47}]
::secs::set EQP {U2 5 1000}

## Slide 11: ::secs::foreach
::secs::foreach v {L {U1 5} {U1 6}} {\…..
::secs::foreach v {U1 5 6}

## Slide 12: Equipment state
Global array EQP
array set EQP {
T3 45000
software {L {A CONCP1} {A 4.433}}
}
proc EQPconnect {} …….
Proc EQPS<num>F<num> {}

## Slide 13: www
secs.sourceforge.net
Hume (www.hume.com)
secslib (japanese) ???

## Slide 14: Demo